## Slide 1
Abstract
Architecture
Methods
Result
Yuan-An Liu, Christopher Hannon, Dong Jin
This work focuses on creating a hybrid testing platform combining electric power simulation with Linux network devices such as hosts and switches. This system supports a distributed communication network using real networking hardware to support high fidelity analysis of communication network applications and their impacts on the power systems. The challenge in designing such a hybrid system is in the synchronization of combining real networking devices to an electric power simulator. We implement a solution for this synchronization challenge through a virtual time system.
A Distributed Virtual Time System for Embedded Linux Devices
References
Christopher Hannon, Jiaqi Yan, Dong Jin: DSSnet: A Smart Grid Modeling Platform Combining Electrical Power Distribution System Simulation and Software Defined Networking Emulation
Christopher Hannon, Neil Getty: Heterogeneous Distributed Embedded Linux System for Hardware-in-the-Loop Smart Grid Testbed
⟵ Virtual Time Manager contains two subprocesses:
The host activity is green part of the diagram. The host can be either Controller, switch or sensor.
The network Coordinator (NC) is red part of the diagram which handles all pausing, resuming and other network communications.
↑ The flow diagram represents the overview of distributed algorithm within the kernel module, VTGPIO, layer.
⟵ Architecture of distributed system composed of 3 communication channels: Ethernet, wireless management, and direct hardware connection with general purpose and router Linux hardware.
The top node
Monitoring machine which is not in Virtual Time.
The bottom nodes
Embedded Linux devices
wireless and wired indicate the connection between switches, router and nodes
⟵ The relationship between distributed systems.
Each node has 2 major layers: VT Manager, Virtual Time kernel.
They are all connected using Ethernet, wireless networking, and direct hardware connection.